## Slide 1
HÖGSKOLAN VÄST
SESSION 1
System Overview, Safety and Image Capture
Understanding the pipeline and building your first dataset
⏱ ~3 hours
Tillsammans förändrar vi.

## Slide 2
Learning Objectives
HÖGSKOLAN VÄST
– Understand the full vision-to-pick pipeline
– Learn robot safety procedures and emergency stop
– Set up the camera station with consistent lighting
– Capture a high-quality image dataset for model training (30–50+ images)
– Understand what makes a good vs bad training image
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 3
Session Agenda
HÖGSKOLAN VÄST
00:00
Welcome & Pipeline Overview
00:30
Teacher Live Demo
00:45
Safety Briefing — every student must acknowledge
01:00
Station Setup — robot, camera, lighting
01:30
Break
01:45
Image Capture — varied arrangements
02:30
Dataset Review as a group
03:00
Wrap-up & preview of Session 2
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 4
The Vision-to-Pick Pipeline
HÖGSKOLAN VÄST
– ① Camera captures an image of the workspace
– ② Segmentation model detects objects and outlines their shapes
– ③ Calibration converts pixel positions → physical mm
– ④ Robot arm moves to the computed pick point and grabs the object
– Each session covers one or two stages of this pipeline.
– By Session 4 you will run the full loop automatically(hopefully).
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 5
Safety Rules — Read Before You Touch the Robot
HÖGSKOLAN VÄST
– Know where the Emergency Stop is — test it before starting
– Keep hands clear of the robot workspace during operation
– Never change robot speed or workspace limits without teacher approval
– Always tell your partner before starting any robot motion
– Report any unusual behaviour (jerky moves, error lights) immediately
– Teacher must approve your first automated pick sequence
– ⚠ Each student must verbally acknowledge these rules before proceeding.
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 6
Station Setup Checklist
HÖGSKOLAN VÄST
Hardware
– Robot powered on and homed
– Basler camera connected and test image captured
– Camera position fixed — top-down, centred on workspace
– Lighting: diffuse, no strong shadows
– Clean, uniform workspace background
– Objects placed within camera field of view
Software / Verify
– Run capture_images.py once
– Verify image is sharp and well-exposed
– Check: objects are fully visible, not cropped
– Check: no mirror reflections from shiny surfaces
– If something looks off — tell the teacher now
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 7
Image Capture — Tips for a Good Dataset
HÖGSKOLAN VÄST
– Capture at least 30–50 images per group
– Vary arrangements: single objects, multiple objects, different positions
– Include edge cases: objects touching, near the border, at angles
– Keep lighting consistent across all captures
– Delete blurry, over-exposed, or poorly-lit images immediately
– Rule of thumb: if you can’t clearly identify the object, the model can’t either.
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 8
What Makes a Good Training Dataset?
HÖGSKOLAN VÄST
– Diversity — many positions, orientations, and arrangements
– Balance — roughly equal images of each object class
– Quality — sharp, well-lit, consistent background
– Volume — more labelled data → better model (diminishing returns)
– Relevance — matches real operating conditions
– Bad data → bad model, no matter how good the algorithm.
– Focus on eliminating shadows and background clutter first.
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 9
HÖGSKOLAN VÄST
Key Takeaway
“The quality of your dataset directly determines the quality of your model. Garbage in, garbage out.”
Tillsammans förändrar vi.
End of Session 1