## Slide 1
HÖGSKOLAN VÄST
SESSION 3
Inference and ArUco Calibration
From pixels to millimetres — bridging the gap between camera and robot
⏱ ~3 hours
Tillsammans förändrar vi.

## Slide 2
Learning Objectives
HÖGSKOLAN VÄST
– Run a trained segmentation model on images and interpret the output
– Understand the pixel-to-mm conversion problem
– Perform ArUco-based calibration to compute mm_per_pixel
– Convert detected object positions from pixels to physical millimetres
– Verify calibration accuracy against a ruler measurement
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 3
Session Agenda
HÖGSKOLAN VÄST
00:00
Recap — we have a model, now what?
00:15
Inference on saved images — confidence threshold exercise
00:45
The calibration problem — pixels vs mm
01:00
Break
01:15
ArUco calibration exercise
02:00
Apply calibration to inference results
02:30
Live camera inference
02:45
Group results + wrap-up
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 4
Running Inference — What the Model Returns
HÖGSKOLAN VÄST
– Input: an image (JPEG/PNG) sent to the Roboflow API
– Output (JSON) for each detected object:
– • class — the class label (e.g. ‘circle’)
– • confidence — model certainty 0.0–1.0
– • points — list of (x, y) polygon vertices in pixels
– From the polygon we compute the centroid (cx, cy) using image moments.
– Exercise: change confidence threshold 0.3 → 0.5 → 0.8
– Observe how detection count changes.
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 5
The Calibration Problem
HÖGSKOLAN VÄST
– The model outputs positions in pixels (e.g. cx=847 px, cy=512 px)
– The robot needs positions in millimetres (e.g. x=215 mm, y=130 mm)
– We need: mm_per_pixel = physical_distance_mm / distance_pixels
– Assumptions that must hold:
– • Camera is fixed between capture and pick
– • Workspace is flat — all objects on the same plane
– • Camera is mounted top-down (no perspective distortion)
– If any assumption is violated, accuracy will degrade.
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 6
ArUco Markers — How Calibration Works
HÖGSKOLAN VÄST
– An ArUco marker is a square fiducial with a unique ID pattern
– We print one at a known physical size (e.g. 50 mm × 50 mm)
– Steps:
– 1. Place the marker flat in the workspace
– 2. Capture an image
– 3. Detect the 4 corner points of the marker in pixels
– 4. Measure the side length in pixels (C0→C1 distance)
– 5. Compute: mm_per_pixel = 50 mm / side_px
– Corner C0 of the marker = work object origin (0, 0)
– All object positions are reported relative to C0.
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 7
Student Exercise — ArUco Calibration
HÖGSKOLAN VÄST
Calibration
– ① Measure the printed marker with a ruler
– → Record the side length in mm
– ② Enter the measurement in the notebook
– MARKER_SIZE_MM = ___
– ③ Run the calibration cell
– → Note mm_per_pixel value
– ④ Record your result in the group log
Verification
– Verification step:
– Place an object at a known distance from C0
– Measure with a ruler → X mm
– Run verification cell
– Compare computed vs measured distance
– Goal: error < 5%
– If > 10% → recheck marker size or camera tilt
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 8
Apply Calibration to Inference Results
HÖGSKOLAN VÄST
– After calibration you have: mm_per_pixel and c0_px (origin in pixels)
– For each detected object centroid (px_x, px_y):
– wobj_x = (px_x − c0_px[0]) × mm_per_pixel
– wobj_y = (px_y − c0_px[1]) × mm_per_pixel
– These coordinates are directly in the robot work object frame.
– No manual offset is needed when the work object is defined at C0.
– Activate with: User(N) on the robot before sending move commands.
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 9
HÖGSKOLAN VÄST
Key Takeaway
“One printed marker, one ruler measurement, and one division turns every pixel in your image into a real-world coordinate the robot understands.”
Tillsammans förändrar vi.
End of Session 3