## Slide 1
HÖGSKOLAN VÄST
SESSION 4
Robot-Guided Pick and Place
Connecting vision to motion — the full autonomous pipeline
⏱ ~3 hours
Tillsammans förändrar vi.

## Slide 2
Learning Objectives
HÖGSKOLAN VÄST
– Connect the complete vision pipeline to the Dobot E6 robot arm
– Execute supervised and autonomous pick-and-place sequences
– Use the ArUco work object frame for accurate positioning
– Log pick results and compute a success rate
– Analyse failures and propose improvements
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 3
Session Agenda
HÖGSKOLAN VÄST
00:00
Recap + Safety Review — mandatory before robot use
00:15
Teacher verifies every station individually
00:45
First supervised picks — teacher present
01:15
Break
01:30
Independent picking — increasing difficulty
02:00
Mixed clutter challenge — 5+ objects
02:30
Final group demo (2 min each)
02:45
Discussion, wrap-up, and reflection
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 4
Safety Review — Robot Section
HÖGSKOLAN VÄST
– ⚠ Review before EVERY robot session
– Emergency stop location confirmed
– Hands and tools clear of workspace before any move
– Robot speed set to a safe value (≤30%)
– Teacher has approved the first pick at your station
– Drop zone is defined and clear
– If the robot moves unexpectedly → press E-stop immediately
– Do not try to catch a falling object with your hands
– Teacher must countersign your station checklist before you begin.
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 5
The Full Pipeline — All Four Steps Together
HÖGSKOLAN VÄST
– ① Capture — Take a fresh image from the Basler camera
– ② Segment — Send image to Roboflow → receive mask polygons
– ③ Compute — Convert centroids to work object coordinates
– wobj_x = (px_x − c0_px[0]) × mm_per_pixel
– ④ Pick — Send MovL command to Dobot E6
– Approach → Descend → Suction ON → Lift → Drop → OFF
– The robot uses User coordinate frame N — C0 of the ArUco marker is (0, 0, 0).
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 6
First Picks — Step by Step
HÖGSKOLAN VÄST
Procedure
– Place ONE object in a clear area
– Run the full pipeline cell by cell
– Observe the pick point on the visualisation
– Teacher approves the target before robot moves
– Record the outcome in your pick log
– Adjust X/Y/Z offsets if needed
– Repeat for 3–5 single-object picks
Recording Results
– Pick Log format:
– Pick# | Class | Conf | Position | Result
– 1 | circle | 0.92 | (45, 30) | ✓
– 2 | square | 0.78 | (80, 55) | ✗ off 8mm
– Track every attempt.
– You will present your success rate at the end.
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 7
Independent Picking — Increasing Complexity
HÖGSKOLAN VÄST
– Level 1 — Single object, centred in workspace
– Level 2 — Two objects: pick the one with higher confidence
– Level 3 — Three objects: pick in order (e.g. largest area first)
– Level 4 — Objects near the workspace boundary
– For each level: run the pipeline → log the result → analyse failures
– If a pick fails, diagnose before continuing:
– • Was the detection correct? (check the visualisation)
– • Was the computed coordinate plausible?
– • Did the suction cup miss the object centroid?
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 8
Mixed Clutter Challenge
HÖGSKOLAN VÄST
– Arrange 5 or more objects — some touching, some overlapping
– Mix all object classes together
– Run the full pipeline and attempt to pick every object
– Discussion questions after your attempt:
– • Which objects were picked successfully?
– • Which were missed or misidentified?
– • Did overlapping objects cause problems?
– • Would a different pick order have worked better?
– • What would need to change for a real factory setup?
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 9
Wrap-up Discussion — Key Questions
HÖGSKOLAN VÄST
– What was the single biggest source of error at your station?
– How did your mm_per_pixel calibration compare to other groups?
– What would you change to improve pick reliability to > 90%?
– Looking further ahead:
– • How would you handle 3D objects (not flat on a surface)?
– • What if a new object type appears that was not in training?
– • How would a real factory system handle lighting changes?
– • What safety certifications would a production robot need?
Vision-Guided Robotic Picking Lab · Högskolan Väst

## Slide 10
HÖGSKOLAN VÄST
Key Takeaway
“Vision-guided robotics is not magic — it is a chain of steps, each introducing a small error. Understanding where errors come from is the first step to eliminating them.”
Tillsammans förändrar vi.
End of Session 4